Online and Adaptive Learning and Optimization for Human-Centered HVAC Systems Operations

Ali Ghahramani

PhD Student, Sonny Astani CEE Department, University of Southern California

January 27, 3:00pm, SLH 102

Abstract:

The common practice of defining operational settings for Heating, Ventilation and Air Conditioning (HVAC) systems in buildings is to use fixed set points, which assume occupants have same and static comfort requirements. However, thermal comfort varies from person to person and also changes due to climatic variations or acclimation, making it dynamic. Thus, thermal comfort has to be monitored over time. Prior research on learning personal thermal preferences and control for optimal HVAC operations has not considered the dynamic behavior of the occupants’ preferences and often used learning and optimization/control methods that are applied to time-invariant systems. In this presentation, I introduce a novel infrared thermography based technique to monitor an individual’s thermoregulation performance and estimate thermal comfort levels by measuring the skin temperature on several points on human face, which has a high density of blood vessels and is not usually covered by clothing.  The observed heterogeneous behavior of facial points was then used to define thermal comfort confidence levels via an unsupervised learning algorithm (a hidden Markov model).  To reduce the need for continuous data collection, a dynamic Bayesian network to quantify dynamic thermal comfort preferences as a function of indoor air temperature is introduced. In order to integrate the time-variant range of preferred indoor air temperatures into the HVAC system control loop, I present several heuristics (via knowledge based approaches) and metaheuristics (via an adaptive hybrid metaheuristic) to design data-driven and adaptive control policies.

Bio:

Ali Ghahramani defended his PhD dissertation in October 2016 within Informatics for Intelligent Built Environments program. His research focuses on the development of methodologies for advanced sensing, adaptive learning, and control methods that capture the systems dynamics with applications in energy conservation and sustainability in buildings. In his research, he takes advantage of the novel advancements in sensing methods and blends collected data with physical models and heuristics to mine and learn system behaviors in order to minimize costs and improve service quality. As a member of the innovation in integrated informatics research group (i-Lab), he conducted interdisciplinary research on state-of-the-art non-intrusive sensing methods for learning building occupants’ preferences and optimal control and optimization methods for improving building energy efficiency and occupants comfort. His research has led to the publication of 14 journal and conference papers and 2 patents. During his graduate studies, he received a M.Sc. in Civil and Environmental Engineering (specialty: Construction Engineering), a M.Sc. in Computer Science (specialty: Data Science), and a M.Sc. in Industrial and System Engineering (specialty: Systems Architecting and Engineering).